| 努力超越 | Strive for surpassing |
| --- | --- |
| 追求卓越 | Go after excellence |

平高集团有限公司 Pinggao Group Co., Ltd.

平高集团有限公司 Pinggao Group Co., Ltd. 地址：中国•河南•平顶山市南环东路22号 Address: No.22, East Nanhuan Road, Pingdingshan, Henan, China 邮编：467001 Postal Code: 467001 销售热线：0375-3506384 Sales hotline: 0375-3506384 服务热线：400 6700 12 Service hotline: 400670012 传真：0375-3506385 Fax.: 0375-3506385 http://www.pinggaogroup.com

储能系统

# Energy Storage System

中国·河南

Henan, China

目录

# Contents

|  | 10 | 储能产业发展 Development of Energy Storage Industry |
| --- | --- | --- |
|  | 16 | 储能系统及解决方案 Energy Storage System and Solutions |
|  | 16 | 集中式可再生能源并网 Centralized Renewable Energy Grid Connection |
|  | 19 | 调频服务 Frequency Modulation Service |
|  | 20 | 削峰填谷 Peak Load Shifting |
|  | 21 | 微电网储能电站 Energy Storage Power Station of Micro-grid |
|  | 21 | 工商业园区储能电站 Energy Storage Power Station of Industrial and Commercial Parks |
|  | 22 | 户用储能 Household Energy Storage |
|  | 22 | 相变储能在电能替代中的应用 Application of Phase-change Energy Storage in Electric Energy Substitution |
|  | 23 | 核心产品 Core Products |
|  | 24 | 箱式储能系统 Box Energy Storage System |
|  | 26 | 户用储能系统 Household Energy Storage System |
|  | 28 | 应急电源车 Emergency Power Supply Vehicle |
|  | 30 | 工程业绩 Project Performance |
|  | 36 | 科研创新 Research and Innovation |
|  | 36 | 科技研发 Research & Development |
|  | 40 | 学术交流 Academic Exchange |

储能产业发展

# Development of Energy Storage Industry

2013年，平高集团按照国家电网公司部署安排，开始调研电池储能技术；

Pinggao Group began to investigate battery energy storage technologies in accordance with the deployments of the State Grid Corporation of China in 2013;

2016年，平高集团把大规模储能做为大力发展的增量业务之一，成立储能筹备领导小组及储能筹备工作，开展储能相关工作；

In 2016, Pinggao Group made large-scale energy storage one of the vigorously developed incremental businesses. It set up a leadership team for energy storage preparation and established energy storage preparation work, and carried out energy storage-related work;

2017年，平高集团成立电力储能事业部，集中优势力量，大力发展储能产业。

In 2017, Pinggao Group established the Power Energy Storage Business Division to concentrate its strengths and vigorously develop the energy storage industry.

由平高集团首次承建的国家863智能微电网项目通过国家科技部验收。

The national 863 smart micro-grid project constructed by Pinggao Group for the first time has passed the acceptance of the Ministry of Science and Technology.

1.	集中式可再生能源并网

1.	Centralized Renewable Energy Grid Connection

| 储能系统及解决方案 Energy Storage System and Solutions 集中式可再生能源并网 Centralized Renewable Energy Grid Connection 风能或太阳能等可再生能源发电具有随机性和波动性 的缺点，通过在风力发电或太阳能发电系统中引入一定星 的储能系统可平滑可再生能源发电输出，减少对电网的冲 击；提高跟踪计划出力能力；另外，有效减少弃光、弃风现象。 Renewable energy generation such as wind energy or solar energy has the disadvantages of randomness and volatility. Introduce the smooth renewable energy generation output of a certain amount of energy storage systems into the wind power generation or solar energy generation systems, so as to reduce the impact on the power grid and improve the ability of tracking schedule output; In addition, it can effectively reduce the PV and wind curtailment. 应用特点: Application characteristics: 1.交流母线连接，适合集中管理； 1. AC busbar connection, suitable for centralized management; 2.减少弃光、弃风，提离经济性； 2. Reduce the PV and wind curtailment to improve economy; 3.跟踪计划调度，提高并网可控性： 3. Track schedule dispatching to improve grid-connected controllability; 4.提离发电预测精度，提升并网友好性。 4. Improve generation prediction accuracy and grid-connected friendliness. |  |
| --- | --- |

| 调度中心 | Dispatching center |
| --- | --- |
| 监控平台 | Monitoring platform |
| 环境检测仪 | Environmental monitoring instrument |
| 光伏逆变器 | PV inverter |
| 储能逆变器 | Energy storage inverter |
| 直流电缆 | DC cable |
| 交流电缆 | AC cable |
| 通讯线 | Communication line |

平滑可再生能源发电输出

# Smooth renewable energy generation output

| 电力系统 Power system 风电功率 Wind power 功率指令 Power instruction 平抑波动控制算法 Fluctuation stabilizing control algorithm 功率指令 Power instruction 能量状态反馈 Energy state feedback 风电场 Wind farm 储能能量管理 Energy management of energy storage 储能系统 Energy storage system 依据实时的风电功率数据和储能系统的能量状态得到储能系统需补偿的功率指令，经过储能 系统的功率补偿，风电和储能系统的总输出功率 得到平抑。 Based on the real-time wind electricity power data and the energy state of the energy storage system, the power instruction to be compensated by the energy storage system is obtained. Through the power compensation of the energy storage system, the total output power of the wind electricity system and energy storage system is stabilized. | 功率/千瓦 Power / kW 平抑前 Before stabilization 指令值 Instruction value 平抑后 After stabilization 电池功率 Battery power 时间/分钟 Time / min 平抑功率波动曲线 Fluctuation Curve of Stabilized Power |
| --- | --- |

跟踪计划出力能力

# Ability of tracking schedule output

| 变流器 Converter 断路器 Circuit breaker 风储合成出力 Integrated output of wind power and energy storage systems 电网 Power grid 数据监控系统 Data monitoring system 风电功率 Wind power 预测系统 Prediction system 风电功率数据、风电预测数据 Wind power data， wind power prediction data 数据处理分析模块 Data processing and analysis module 利用电池储能系统的双向功率能力弥补实际风电功率的溢出或不足，使风储合成出力功率数据与风电功率预测数据之间的日预测最大误差满足标准要求。 The bidirectional power capability of the battery energy storage system is used to make up the overflow or insufficiency of the actual wind power, so that the maximum daily prediction error between the integrated output power data of wind power and energy storage systems and the wind power prediction data meets the standard requirements. | 功率/千瓦 Power / kW 预测计划指令： Predicted schedule instructions: •0-10分钟功率指令值12MW •10-24分钟功率指令值14MW •24-45分钟功率指令值18MW •0-10 min, power instruction value: 12 MW •10-24 min, power instruction value: 14 MW •24-45 min, power instruction value: 18 MW 平抑前 Before stabilization 指令值 Instruction value 平抑后 After stabilization 电池功率 Battery power 时间/分钟 Time / min 跟踪计划出力曲线 Curve of tracking schedule output |
| --- | --- |

| 减少弃光、弃风现象 | Reduce the PV and wind curtailment |
| --- | --- |
| 电力 | Power |
| 电力负荷（虚线） | Power load (dotted line) |
| 充电 | Charge |
| 放电 | Discharge |
| 来自电网的电力（实线） | Power from power grid (full line) |
| 削峰值 | Peak clipping value |
| 储能系统能够在弃风、弃光限电时 段存储少星电蚩，在非限电时段上 网，获得更多的高峰负荷收益。 | The energy storage system can store a small amount of electricity during the PV curtailment, wind curtailment and power brownout, and access to the Internet during non-power-brownout periods to obtain more peak load revenue. |
| 增加储能系统实际功率 | Improve the actual power of energy storage system |
| DCDC充放电功率 | DCDC charging/discharging power |
| 未增加储能系统实际功率 | Fail to improve the actual power of energy storage system |
| 某光伏电站增加储能系统后发电情况 | The Generation Condition of a PV Power Station after Increasing Its Energy Storage Systems |

2.	调频服务

2.	Frequency Modulation Service

| 调频服务 Frequency Modulation Service 传统电力系统在稳定电网方面存在响应慢的缺 点，引入电池储能系统后，可辅助传统电力系统 及AGC设备，快速响应调频、调压指令，提高电 网稳定性。 Traditional power systems have the disadvantage of slow response to the stability of the power grid. After the battery energy storage system is introduced, traditional power systems and AGC equipment can be assisted to quickly respond to frequency modulation and voltage regulation instructions and improve the stability of the power grid. 应用特点： Application characteristics: 1.既可以实现一次调频，又可以实现二次调频; 1. Both the primary and secondary frequency modulation can be achieved; 2.有效提高电网频率稳定性； 2. Improve the frequency stability of the power grid; 3.具有快速动态响应速度。 3. Have a rapid dynamic response speed. |  |
| --- | --- |

| 调度中心 | Dispatching center |
| --- | --- |
| 火电厂 | Thermal power plant |
| 监控平台 | Monitoring platform |
| 储能逆变器 | Energy storage inverter |
| 电网 | Power grid |
| 直流电缆 | DC cable |
| 交流电缆 | AC cable |
| 通讯线 | Communication line |

3.	削峰填谷

3.	Peak load shifting

| 削峰填谷 | Peak Load Shifting |
| --- | --- |
| 调度中心 | Dispatching center |
| 功率回路 | Power circuit |
| 监控回路 | Monitoring circuit |
| 储能变流器1 | Energy storage converter 1 |
| 蓄电池1 | Storage battery 1 |
| 储能变流器n | Energy storage converter n |
| 蓄电池n | Storage battery n |
| 监控平台 | Monitoring platform |
| 负荷配电柜 | Load power distribution cabinet |
| 负荷端 | Load side |
| 电网 | Power grid |
| 变压器 | Transformer |

| 适用场景 | Applicable occasion |
| --- | --- |
| 工商业用户 | Industrial and commercial users |
| 1.有基本电费制度，超过基本电费的部分电 费成倍增加； 2.节省变电设备升级改造的费用； 3.谷电时段充电，峰电时段放电，利用电价 差套利； 4.港口，地铁站，高耗能企业等。 | 1. There is a basic electric charge system. A portion of electric charges exceeding the basic electric charge is exponentially increased; 2. Save the cost for upgrading and transformation of substation equipment; 3. Charge during the valley electric period and discharge during the peak electric period, and seek for arbitrage by using the electric charge difference; 4. Ports, subway stations and high energy-consuming enterprises, etc. |
| 电网公司 | Power grid companies |
| 1.高峰期负荷对电网冲击比较厉害，可能造 成电网的损害； 2.节省升级维护电网的费用； 3.不以短期的投资回报为目的。 | 1. In the peak period, the impact of the load on the power grid is more severe and may cause damage to the power grid; 2. Save the cost of upgrading and maintaining the power grid; 3. Do not aim at short-term investment returns |

4.	微电网储能电站

4.	Energy Storage Power Station of Micro-grid

| 微电网储能电站 Energy Storage Power Station of Micro-grid 涵盖分布式并网发电、离网电站、光储充一体，利用微电网的实时调度与控制实现整个系统的高效、安全运转。 It covers distributed grid-connected power generation, off-grid power station and integrated PV, energy storage and charging systems. It uses the real-time dispatching and control of the micro-grid to achieve highly efficient and safe operation of the entire system. 应用特点： Application characteristics: 1.支持并网、离网运行模式，离网模式下提供u/f支撑； 1. Support grid-connected and off-grid operation modes, and provide the u/f support under the off-grid mode; 2.平滑风电、光伏出力波动，提高供电质量； 2. Smooth the wind power and PV output fluctuation and improve the quality of power supply; | 电网 Power grid 能量控制模块 Energy control module 能量管理系统 Energy management system 可控负载 Controllable load 用户负载 User load 风力发电系统 Wind power generation system 光伏发电系统 PV power generation system 储能系统 Energy storage system |
| --- | --- |

3.融合新能源发电、混合储能、充电桩、太阳能热水、新能源汽车等元素;

# 3. Integrate new energy generation, hybrid energy storage, charging piles, solar hot water, new energy vehicles and other elements;

4.大电网故障条件下能够实现24小时可靠供电。

# 4. Be able to provide reliable power supply for 24 hours under major faults of the power grid.

# 5.	工商业园区储能电站

# 5.	Energy Storage Power Station of Industrial and Commercial Parks

| 太阳能电池板 | Solar panel |
| --- | --- |
| 光伏逆变器 | PV inverter |
| 电网 | Power grid |
| 变压器 | Transformer |
| 储能变流器 | Energy storage converter |
| 电池组 | Battery assembly |
| 配电柜 | Power distribution cabinet |
| 交流充电桩 | AC charging pile |
| 小轿车 | Car |
| 直流充电桩 | DC charging pile |
| 小轿车 | Car |
| 大客车 | Coach |

应用特点：

# Application characteristics:

1.光伏发电与储能配合为本地负荷提供电力；

# 1. PV power generation cooperates with energy storage to provide power for local loads;

2.充分利用太阳能发电为充电站提供能源，减少电动汽车充电容虽对电网冲击;

# 2. Make full use of solar energy generation to provide energy for charging stations, and reduce the impact of the charging capacity of electric vehicles on the power grid;

3.可并网、离网运行，无缝切换；

# 3. Support grid-connected or off-grid operation with seamless switchover;

4.离网状态下储能系统提供U/f源；

# 4. The energy storage system can provide the U/f source under the off-grid state;

5.利用储能系统削峰填谷。

# 5. Realize the peak load shifting with the energy storage system.

# 6.	光储充一体式电站

# 6.	Integrated Power Station of PV, Energy storage and Charging

| 光伏作为微电网运行状态下的主电源，储能用于建立电网电压，并对光伏发电量不足时进行补充和夜晚、阴雨天时的供电。在光伏和储能都无法进行输出时，系统接入电网给充电机进行供电。 PV is the main power supply under the operating state of the micro-grid. Energy storage is used to establish the grid voltage and supplement the electricity when the PV generating capacity is insufficient, as well as supply power at night and in rainy days. When neither PV nor energy storage can conduct output, the system is connected to the power grid to supply power to the charger. 应用特点： Application characteristics: 1.延缓和减少电动汽车充电对电网的扩容要求； 1. Delay and reduce the capacity expansion requirements of electric vehicle charging to the power grid; 2.通过充电时间、充电功率的合理分配，削峰填谷，缓解电网的峰谷差。 2. Through the reasonable distribution of charging time and charging power, the peak load shifting is performed to ease the peak-to-valley difference in the power grid. 适用行业： Applicable industries: 实行峰谷电价差（且电价差较大）、峰值时段有充电需求的场合。例如电动公交场站、（工商业园区、高档社区）停车场。 Occasions implementing the peak-valley electric charge difference (with a bigger electric charge difference) and having charging needs in the peak period. Such as electric bus stations and parking lots (in industrial and commercial parks and high-end communities). | 公共电网 Public power grid 400V交流母线 400V AC busbar |
| --- | --- |

7.	户用储能

# 7.	Household Energy Storage

| 针对家庭、交通照明等用户开发的太阳能发电储能供电系统。 A solar energy generation, storage and power supply system developed for users such as households and transportation lighting. 系统主要由太阳能电池组、太阳能控制器、并离网逆变器、蓄电池组、电池管理系统、能量控制器等组成，可实现能源在吸收、转换、储存及使用环节自动化，节约用电成本，实现绿色环保的目的。 The system composes of the solar battery, solar controller, grid-connected and off-grid converter, storage battery, battery management system and energy controller. It can achieve automatic absorption, conversion, storage and use of energy sources and save electric costs, as well as realize the goal of green and environmental protection. 应用特点 Application characteristics 1.高效率、高可靠性、高智能，备电时间长； 1. High efficiency, high reliability, high intelligence and long power preparation time; 2.智能自动切换，可实现无人值守； 2. Intelligently automatic switchover and be able to realize unmanned operation; 3.人性化报警功能，完善在线保护； 3. Humanized alarm function and improve on-line protection 4.Wifi通讯，无线控制，实现远程操作； 4. Wifi communication and wireless control, realizing remote operations; 5.可联网，可通过电脑和手机查看、控制。 5. Be able to be connected to the Internet and be checked and controlled through computers and phones. | 光伏组件 PV module 直流 DC 单相离网太阳能控制逆变器一体机 Single-phase off-grid solar energy control converter AIO 交流 AC 交流负载 AC load 市电 Power frequency AC 油机 Oil engine 蓄电池组 Storage battery |
| --- | --- |

8.	相变储能在电能替代中的应用

8.	Application of Phase-change Energy Storage in Electric Energy Substitution

平高集团依托国内先进的相变储能技术，以分布 式能源站为基础，以能源管理系统为纽带，构建多 能互补的区域能源供应体系，提供能源综合服务。

Based on distributed energy stations and with energy management systems as the link, Pinggao Group relies on domestic advanced phase change energy storage technology to build a multi-functional and complementary regional energy supply system and provide integrated energy services.

相变蓄热系统采用多元复合相变蓄热材料，结合独创的高效换热器设计。产品具有蓄热量大、低成本、零排放、模块化、自动化等持点。

The phase change heat storage system uses multiple composite phase change heat storage materials and combines original high efficient heat exchanger design. The product has advantages of large heat storage, low cost, zero discharge, modularization and automation.

蓄热量大：最大单体蓄热设备蓄热星达2500kWh,可供10000-12000平米；

Large heat storage: maximum heat storage of the single heat storage equipment can reach 2,500 kWh and heat can be provided for an area of 10,000 - 12,000 m2;

蓄热及放热迅速：最快实现1小时充放；

Rapid heat storage and discharge: the fastest (1-hour) storage and discharge can be reached;

经济效益：节约运行费用40%-70%。

Economic effectiveness: save operation fee by 40% - 70%.

| 移动热源 Mobile heat source | 谷电供暖/煤改电/电能替代 Valley electric heat supply / coal to electricity / electric power alternative |
| --- | --- |
| 农产品烘干 Agricultural product drying | 工业余热废热利用 Usage of industrial afterheat and waste heat |
| 电厂调峰 Peak load regulating of power plant | 弃风弃光供暖 Wind and PV curtailment for heat supply |

1.	箱式储能系统

1.	Box Energy Storage System

主要特点：

# Main characteristics:

1.标准化、模块化模组设计，系统容量灵活配置；

# 1. Standardization, modular module design and flexible configuration of system capacity;

2.系统高一致性；

# 2. High consistency of the system;

3.激光焊接工艺，系统高可靠性；

# 3. Laser welding process and high system reliability;

4.配置动环监控、温控和消防系统，保证系统安全可靠运行;

# 4. Configuration of the power and environment monitoring, temperature control and fire protection systems to ensure safe and reliable operation of the system;

5.BMU内置，高精度采集，自带主动/被动均衡功能；

# 5. Built-in BMU, highly accurate acquisition and self-equipped active/positive balancing function;

6.支持RS485/CAN通信；

# 6. Support RS485/CAN communication;

7.SOC、SOH等实时数据状态可视化；

# 7. Visualized states of real-time data such as SOC and SOH;

8.支持EMS远程调度管理。

# 8. Support EMS remote dispatching management.

| 型号 Model | 250kW/1WMh | 1MW/5MWh | 500kW/1MWh | 1MW/1MWh |
| --- | --- | --- | --- | --- |
| 直流侧参数 Parameters at DC side |
| 电池容星 Battery capacity | 1.176MWh | 5.376MWh | 1.036MWh | 1.036MWh |
| 额定电压 Rated voltage | 588V | 672V | 720V | 720V |
| 电压范围 Voltage range | 523V 〜703V | 570V 〜840V | 560V 〜820V | 560V 〜820V |
| 电池类型 Battery type | 铅炭电池 Lead carbon battery | 铅炭电池 Lead carbon battery | 磷酸铁锂电池 Lithium-ion ferrous phosphate battery | 磷酸铁锂电池 Lithium-ion ferrous phosphate battery |
| 交流测参数（并网模式） Parameters at AC side (grid-connected mode) |
| 额定功率 Rated power | 250kW | 1MW | 500kW | 1MW |
| 额定电压 Rated voltage | 400V | 400V | 400V | 400V |
| 电压范围 Voltage range | 400 ±10%(可调） 400 ±10% (adjustable) | 400 ±10%(可调） 400 ±10% (adjustable) | 400 ±10%(可调） 400 ±10% (adjustable) | 400 ±10% (可调） 400 ±10% (adjustable) |
| 过载能力 Overload capacity | 1.1 | 1.1 | 1.1 | 1.1 |
| 额定频率 Rated frequency | 50Hz | 50Hz | 50Hz | 50Hz |
| 频率范围 Frequency range | 49.5Hz〜51 Hz(可调） 49.5Hz〜51 Hz (adjustable) | 49.5Hz 〜51 Hz(可调) 49.5Hz 〜51 Hz (adjustable) | 49.5Hz 〜51 Hz(可调） 49.5Hz 〜51 Hz (adjustable) | 49.5Hz 〜51 Hz(可调） 49.5Hz 〜51 Hz (adjustable) |
| 功率因数 Power factor | 0.9(超前)0.9(滞后） 0.9 (lead) 0.9 (lag) | 0.9(超前)0.9(滞后) 0.9 (lead) 0.9 (lag) | 0.9(超前)0.9(滞后） 0.9 (lead) 0.9 (lag) | 0.9(超前)0.9(滞后） 0.9 (lead) 0.9 (lag) |
| 交流测参数（孤岛模式） Parameters at AC side (isolated island mode) |
| 额定功率 Rated power | 250kW | 1MW | 500kW | 1MW |
| 额定电压 Rated voltage | 400V | 400V | 400V | 400V |
| 电压范围 Voltage range | 400±5%(可调） 400 ±5% (adjustable) | 400±5%(可调） 400 ±5% (adjustable) | 400 ±5%(可调） 400 ±5% (adjustable) | 400±5%(可调） 400 ±5% (adjustable) |
| 额定频率 Rated frequency | 50Hz | 50Hz | 50Hz | 50Hz |
| 功率因数 Power factor | 0.9(超前)0.9(滞后） 0.9 (lead) 0.9 (lag) | 0.9(超前)0.9(滞后) 0.9 (lead) 0.9 (lag) | 0.9(超前)0.9(滞后） 0.9 (lead) 0.9 (lag) | 0.9(超前)0.9(滞后） 0.9 (lead) 0.9 (lag) |
| 系统参数 System parameter |
| 交流接入方式 AC connecting mode | 三相五线 Three-phase five-wire | 三相五线 Three-phase five-wire | 三相五线 Three-phase five-wire | 三相五线 Three-phase five-wire |
| 集装箱数星 Number of containers | 1 个(45HQ) 1 (45HQ) | 4 个(45HQ)1 个(10GP) 4 (45HQ), 1 (10GP) | 1 个(30HQ) 1 (30HQ) | 1 个(35HQ) 1 (35HQ) |
| 防护等级 IP grade | IP54 | IP54 | IP54 | IP54 |
| 噪声 Noise | <65B | <65B | <65B | <65B |
| 工作环境温度 Operating ambient temperature | -20°C~50°C | -20°C-50°C | -20°C-50°C | -20°C~50°C |
| 存储环境温度 Storage ambient temperature | -40°C-65°C | -40°C-65°C | -40°C-65°C | -40°C-65°C |
| 允许相对湿度 Allowable relative humidity | 5% 〜95% | 5% 〜95% | 5% 〜95% | 5% 〜95% |
| 通讯方式 Communication mode | 以太网、RS485、 CAN2.0 Ethernet, RS485, CAN2.0 | 以太网、RS485、 CAN2.0 Ethernet, RS485, CAN2.0 | 以太网、RS485、 CAN2.0 Ethernet, RS485, CAN2.0 | 以太网、RS485、 CAN2.0 Ethernet, RS485, CAN2.0 |

2.	户用储能系统

2.	Household Energy Storage System

壁挂式（容量：1kWh-5kWh）

Wall-mounted (capacity: 1 kWh-5 kWh)

| 落地式（容量：6.5kWh-32kWh） Floor-type (capacity: 6.5 kWh-32 kWh) | 产品简介： Product introduction: 户用储能产品是平高集团针对家庭场景下的储能 及设备开发的储能电源产品。该系列电池模块是一种 智能型无人值守储能电源产品，支持多个模块并联使用，电池模块可以按照预定的通信协议与其他电器设 备进行通讯。 Household energy storage products are energy storage power products developed by Pinggao Group for energy storage and equipment in a home setting. This series of battery modules is an intelligent unattended energy storage power product that supports the parallel use of multiple modules. The battery module can communicate with other electrical equipment in accordance with a predetermined communication protocol. 主要特点： Major characteristics: 1.高安全性、高能量密度和优良的循环性能； 1. High-level safety, high energy density and excellent cycle performance; 2.高性能的电池管理系统BMS,保证电池的安全； 2. Battery management system (BMS) with high performance to ensure the safety of batteries; 3.全智能设计，配置集中监控模块进行数据交换； 3. Fully intelligent design and configuration of centralized monitoring modules for data exchange; 4.精确的SOC及SOH算法，提高系统的可调度 性； 4. Accurate SOC and SOH algorithms, and improve the schedulability of the system; 5.多个电池单体灵活配置，提高输出功率和容量； 5. Multiple batteries are flexibly configured to increase output power and capacity; 6.内置多种通讯模式，支持主流储能变流器通讯 兼容。 6. Internally install multiple communication modes to support the communication compatibility of mainstream energy storage converters. |
| --- | --- |

| 典型户用储能参数 Typical Household Energy Storage Parameters |
| --- |
| 容星 Capacity | 4kWh | 6.5kWh | 8kWh | 12kWh |
| 电池类型 Battery type | 三元锂电 Ternary lithium battery | 三元锂电 Ternary lithium battery | 三元锂电 Ternary lithium battery | 三元锂电 Ternary lithium battery |
| 交流输出 AC output |
| 额定输出功率 Rated output power | 2kW | 2kW | 2kW | 5kW |
| 输出电压 Output voltage | 220/230/240Vac | 220/230/240Vac | 100/110/120V； 220/230/240Vac | 100/110/120V； 220/230/240Vac |
| 输出频率 Output frequency | 50Hz/60Hz | 50Hz/60Hz | 50Hz/60Hz | 50Hz/60Hz |
| 过载能力 Overload capacity | 120%〈负载 <130% @10min; 130%〈负载 <150% @10s 120%〈load <130% @10min; 130%〈load <150% @10s | 120%〈负载 <130% @10min; 130%〈负载 <150% @10s 120%〈load <130% @10min; 130%〈load <150% @10s | 120%〈负载 <130% @10min; 130%〈负载 <150% @10s 120%〈load <130% @10min; 130%〈load <150% @10s | 120%〈负载 <130% @10min; 130%〈负载 <150% @10s 120%〈load <130% @10min; 130%〈load <150% @10s |
| UPS功能 UPS function | 是 Yes | 是 Yes | 是 Yes | 是 Yes |
| 离并网功能 Off-grid and grid-connected functions | 离并网兼可 Off-grid and grid-connected functions are both available | 离并网兼可 Off-grid and grid-connected functions are both available | 离并网兼可 Off-grid and grid-connected functions are both available | 离并网兼可 Off-grid and grid-connected functions are both available |
| 最大功率 Maximum power | 92%(>70% 负载） 92%(>70% load） | 92%(>70% 负载） 92%(>70% load） | 92%(>70% 负载） 92%(>70% load） | 92°/。(>70% 负载） 92%(>70% load） |
| 交流充电 AC charging |
| 输入电压 Input voltage | 88 〜264Vac | 88 〜264Vac | 88 〜264Vac | 88 〜264Vac |
| 输入频率 Input frequency | 50/60Hz±5Hz | 50/60Hz±5Hz | 50/60Hz±5Hz | 50/60Hz±5Hz |
| 最大充电功率 Maximum charging power | 600W | 2.4kW | 2.4kW | 5kW |
| 光伏充电 PV charging |
| 最大输入功率 Maximum input power | 1.5kW | 2.4kW | 2.4kW | 2.4kW |
| 启动电压 Startup voltage | 75Vdc | 75Vdc | 75Vdc | 75Vdc |
| MPPT 数 MPPT numbers | 2 | 2 | 2 | 2 |
| MPPT输入电压 MPPT input voltage | 75 〜140Vdc | 75 〜140 Vdc | 75 〜140 Vdc | 75 〜140 Vdc |
| 最大输入电压 Maximum input voltage | 150 Vdc | 150 Vdc | 150 Vdc | 150 Vdc |
| MPPT功率 MPPT power | 99.50% | 99.50% | 99.50% | 99.50% |
| 最大功率 Maximum power | >96% | >96% | >96% | >96% |
| 太阳能充电模式 Solar energy charging mode | MPPT | MPPT | MPPT | MPPT |
| 常规 Regular |
| 工作环境温度 Operating ambient temperature | 0°C~45°C | 0°C~45°C | 0°C~45°C | 0°C~45°C |
| 允许相对湿度 Allowable relative humidity | 5%~90% | 5% 〜90% | 5% 〜90% | 5%~90% |
| 产品尺寸 Product size | L510*W270*H600mm | L779*W347*H912mm | L779*W350*H912mm | L779*W472*H928mm |

3.	应急电源车

3.	Emergency Power Supply Vehicle

主要特点：

# Major characteristics:

1.容量大，工作时间长，车载电池300kWh;

# 1. Large capacity, long working time and on-board battery of 300 kWh;

2.多种工作模式，自带车载混合变换系统：

# 2. Multiple working modes and self-equipped on-board hybrid transformation system:

输入：交流/直流：60kW

Input: AC/DC: 60 kW

输出：直流60kW@750V

Output: DC: 60 kW @750V

交流：3相30kW

AC: Three-phase: 30 kW

3.具有良好的环境适应性，可保证设备全天候正常工作，安全实用;

# 3. Good environmental adaptability； it can ensure normal operation of equipment around the clock; safe and practical;

4.电源控制系统先进，确保供电运行可靠；

# 4. Advanced power supply control system; ensure reliable operation of power supply;

5.节能环保，工作时无污染，无矂声。

# 5. Energy saving and environmental protection, no pollution at work and free of noise.

| 应用 | Application |
| --- | --- |
| 应急抢修 | Emergency repair |
| 应急救护 | Emergency rescue |
| 应急交流放电 | Emergency AC discharging |

系统原理

System principle

| 你变系统：功率可定制 | Inverter system: power can be customized |
| --- | --- |
| 充电及放电系统：60kW@750V含触摸屏、控制单元绝缘监测单位等。 | Charging and discharging system:60 kW @750V; include touch screen, control unit and insulation monitoring unit, etc. |
| 交流接口：交流输入采用插接方式 | AC interface: the plug-in method is used for AC input |
| 直流充电接口： 充电枪：对外充电，也可对内充电 充电座：可接受外部充电 | DC charging interface: Charging gun: internal and external charging Charging base: external charging is acceptable |
| 电池组：300kWh 一组电池，一套BMS系统 | Battery: 300 kWh A set of batteries and a set of BMS |

车辆选型

# Vehicle Selection

| 项目 Project | 技术参数指标 Technical parameter indexes |
| --- | --- |
| 整车外形 Vehicle appearance | 5995mmX2150mmX2760mm |
| 厢内尺寸 Compartment size | 4100mmX2020mmX1770mm |
| 总质量 Gross mass | 7100kg |
| 整备质量 Unladen mass | 6905kg |
| 轴距 Wheel base | 3300mm |
| 最高车速 Maximum speed | 95km/h |
| 续航里程 Endurance mileage | ≥150km（40km/h等速行驶） ≥150Km（constant speed drive: 40km/h） |
| 底盘型号 Chassis model | EQ1070GTEVJ3载货汽车底盘 EQ1070GTEVJ3 cargo truck chassis |

| 车辆需求 Vehicle demand 载重要求：5370kg Load requirement: 5370 kg 空间要求：300x2000x1760 Space requirement: 300x2000x1760 |  |
| --- | --- |

工程业绩

# Project Performance

南方电网调峰调频电站

# Peak and Frequency Modulation Power Station of the Southern Power Grid

该项目为国家863课题项目，主要用来验证储能系统在调峰调频领域的作用。该项目包含2MW/2MWh电 池储能系统，采用链式储能结构、开发式二次系统控制平台，并采用先进的储能系统电池管理技术：高性能 嵌入式控制器，稳定的实时操作系统，高效数据采集，图形化软件编程系统，友善的人机界面。

The project is a national 863 project, which is mainly used to verify the role of energy storage systems in peak and frequency modulation. The project includes a 2MW/2MWh battery energy storage system, a chain-type energy storage structure, a developed secondary system control platform and an advanced battery management technology for energy storage systems: high-performance embedded controllers, stable real-time operating systems, efficient data acquisition, graphical software programming systems and friendly man-machine interfaces.

|  | 监控系统 Monitoring system 上位机 Upper computer |
| --- | --- |

青海6MW光储独立微电网

# Qinghai 6MW PV and Energy Storage Independent Micro-Grid

该项目位于青海省杂多县新县城处于高海拔地区。微电网中不含有任何火电或水电机组，仅以光伏发电为能量来源，完全由储能作为电网支撑向杂多县新县城配电系统供电；系统运用6台储能变流器离网并联，实现了在无大电网支撑下多台储能变流器并联、光储互补协调控制的技术创新；储能系统在保障供电功率平稳和夜间正常供电的同时，也避免了独立光储系统的弃光、断电等问题。

The project is located in the high-altitude area of the new county area of Zadoi County, Qinghai. The micro-grid does not contain any thermal power or hydropower units. its energy source only comes from PV power generation and the power is fully supplied by the energy storage as the power grid support to the power distribution system of the new county area of Zadoi County; the system uses 6 sets of energy storage converters for off-grid connection in parallel, achieving the technical innovation of the parallel connection of multiple energy storage converters and complementary coordination control of PV and energy storage under the circumstance of no support of large grid; while the energy storage system guarantees stable power and normal power supply at night, it avoids PV curtailment, blackout and other issues of independent PV and energy storage systems.

|  | 北京乔波滑雪馆屋顶光储项目 Roof PV and Energy Storage Project of Beijing Qiaobo Ski Dome 该项目位于北京市乔波滑雪馆，充分利用滑雪馆屋顶，装设光伏发电容量为3MWp，可再生能源发电与储能结合，为滑雪场负荷供电。储能系统为300kW/1MWh，储能系统不仅可以配合光伏发电，提高控制室能源利用率，而且可以当做应急电源使用，提高电能质量。 The project is located at Qiaobo Ski Dome, Beijing. The roof of the ski dome is full made use and is equipped with a PV with a generating capacity of 3 MWp. The combination of renewable energy generation and energy storage will provide power for the ski resort. The energy storage system is 300 kW/1 MWh. It can not only cooperate with PV power generation, improve the energy utilization efficiency of the control room, but also be used as an emergency power supply to improve power quality. |
| --- | --- |

房山工厂储能削峰填谷项目

# Energy Storage and Peak Load Shifting Project of Factories in Fangshan

该项目位于北京市房山区某工厂，该工厂峰谷电价差较大，利用储能实现用电的削峰填谷，减少电费开支。该项目储能系统为375kw/750kWh,使用锂离子电池，集成为20尺集装箱，安装方便快捷。储能不仅能 实现削峰填谷，同时能够跟踪负荷曲线，实现需量电费管理。

The project is located at a factory in Fangshan District, Beijing. The factory's peak-valley electric charge difference is relatively large. It uses the energy storage to achieve peak load shifting of electricity utilization and reduce electricity expenses. The project's energy storage system is 375 kw/750 kWh, and uses lithium-ion batteries, and they are integrated into a 20-foot container that is easy to install. The energy storage can not only achieve peak load shifting, but also track the load curve and realize the management on demand charges.

| 时间 | Time |
| --- | --- |

| 主配电间 | Main power distribution room |
| --- | --- |
| 充电桩 | Charging pile |
| 电网 | Power grid |
| 主配变压器 | Main distribution transformer |
| 变压器断路器 | Circuit breaker of transformer |
| 工厂总用电负荷采集点 | Acquisition point of the total power load of factories |
| 宿舍 | Dormitory |
| 换热站 | Heat exchange station |
| 泵房 | Pump house |
| 综合楼 | Comprehensive building |
| 储能集装箱 | Energy storage container |
| 集装箱变压器 | Container transformer |
| 集装箱交流侧输出采集点 | Output acquisition point at the AC side of the container |
| PCS交流侧输出采集点 | Output acquisition point at the AC side of the PCS |
| 空调1 | Air conditioner 1 |
| 空调2 | Air conditioner 2 |
| 风机 | Wind turbine |
| 监控及BMS系统 | Monitoring and BMS |
| PCS柜 | PCS cabinet |
| 1#分支 | 1# branch |
| 2#分支 | 2# branch |
| 3#分支 | 3# branch |
| 4#分支 | 4# branch |
| 5#分支 | 5# branch |
| 6#分支 | 6# branch |
| 1#电池簇 | 1# battery cluster |
| 2#电池簇 | 2# battery cluster |
| 3#电池簇 | 3# battery cluster |
| 4#电池簇 | 4# battery cluster |
| 5#电池簇 | 5# battery cluster |
| 6#电池簇 | 6# battery cluster |

科技研发

# Research & Development

平高集团始终坚持“战略性开发与适应性开发相结合，引进技术与自主创新并举，产学研相结合”的产品 开发方针，不断提升产品的技术性能。通过一系列产品的自主开发，培养和锻炼出一批业务能力强、专业素质 高、经验丰富的技术人员，造就出国内一流的研发队伍。

Pinggao Group always adheres to the product development policy of “combining strategic development with adaptive development, promoting technology introduction and independent innovation simultaneously, and integrating production, learning and research” to continuously improve the technical performance of the product. Through the independent development of a series of products, we cultivate and train a group of technical personnel with strong business abilities, high professional qualifications, and rich experience, creating a first-class R&D team in the country.

在储能技术研究领域，牵头开展河南省重大科技专项项目1项，参与国家电网公司总部管理科技项目4 项，承担国家重点研发计划项目“MW级先进飞轮储能关键技术研究”子课题研究工作。重点攻关高可靠长寿命锂离子电池技术和MW级储能系统集成技术。

In the field of energy storage technology research, it takes the lead in carrying out 1 major science and technology project in Henan Province, participates in 4 science and technology projects managed by the headquarters of the State Grid Corporation of China, and undertakes the sub-project research work of the national key R&D project — “Key Technology Research on MW-class Advanced Flywheel Energy Storage”. It focuses on the high-reliability long-life lithium-ion battery technology and MW-class energy storage system integration technology.

| 高低温环境设备 High/low temperature environmental equipment | 高低温环境设备 High/low temperature environmental equipment |
| --- | --- |
| 高低温环境设备 High/low temperature environmental equipment | 电池特性监控分析系统 Battery characteristic monitoring and analysis system |

电池测试设备

Battery test equipment

| 科研人员正在进行研发 Researchers are performing R&D. | 新产品鉴定会 New product appraisal meeting | 科技大会 Sci-Tech Conference |
| --- | --- | --- |

学术交流

# Academic Exchange

平高集团坚持创新驱动发展，与中国电力科学研究院、中国科学院、全球能源互联网研究院、清华大学、 西安交通大学等单位建立合作关系，在电池储能、压缩空气储能、飞轮储能、商业楼宇用氢、超导储能等领域 开展合作交流。

Pinggao Group adheres to innovation-driven development and establishes partnerships with the China Electric Power Research Institute, the Chinese Academy of Sciences, the Global Energy Interconnection Research Institute, Tsinghua University, Xi'an Jiaotong University and other units to carry out cooperation and exchange in the fields of battery energy storage, compressed-air energy storage, flywheel energy storage, hydrogen for commercial buildings and superconducting energy storage.

| 日本东芝公司 | TOSHIBA (Japan) |
| --- | --- |
| 技术交流钛酸锂电池及储能系统 | Technical exchange of LTO batteries and energy storage systems |
| 日本日立公司 | HITACHI (Japan) |
| 技术交流电池及储能系统 | Technical exchange of batteries and energy storage systems |
| 美国普威公司 | Powin (US) |
| 技术交流电池管理系统 | Technical exchange of battery management systems |
| 德国Fraunhofer-Gesellschaft | Fraunhofer-Gesellschaft (Germany) |
| 技术交流 | Technical exchange |
| 德国OLI Systems GmbH | OLI Systems GmbH (Germany) |
| 技术交流电池及储能系统 | Technical exchange of batteries and energy storage systems |
| 平高集团有限公司 | Pinggao Group Co., Ltd. |
| 中国科学院 | Chinese Academy of Sciences |
| 技术交流超导储能、飞轮储能、压缩空气储能 | Technical exchange of superconducting energy storage, flywheel energy storage and compressed-air energy storage |
| 中国电科院 | China Electric Power Research Institute |
| 合作研发高可靠性长寿命电池及兆瓦级电池储能系统 | Cooperative R&D of high-reliability long-life batteries and MW-class battery energy storage system |
| 全球能源互联网研究院 | Global Energy Interconnection Research Institute |
| 合作研发商业楼宇储氢项目 | Cooperative R&D of commercial building hydrogen storage projects |
| 清华大学 | Tsinghua University |
| 合作研发国家重点研发计划项目MW级飞轮储能关键技术 | Cooperative R&D of the national key R&D project — Key Technology of MW-class Flywheel Energy Storage |
| 西安交通大学 | Xi'an Jiaotong University |
| 平高西交大联合研究院 | Pinggao-Xi'an Jiaotong University Union Institute |

| 与清华研究院座谈会 Symposium with the graduate school of Tsinghua University | 与西交大研究院座谈会 Symposium with the graduate school of Xi'an Jiaotong University |
| --- | --- |
| 与中科院过程所专家进行储能技术交流 Energy storage technical exchange with experts from Institute of Process Engineering, Chinese Academy of Sciences | 与美国普威公司专家进行技术交流 Technical exchange with experts from Powin (US) |
| 与北京博瑞公司进行储能技术交流 Energy storage technical exchange with Beijing Borry Technology Development Co., Ltd. | 与日立公司专家进行技术交流 Technical exchange with experts from HITACHI (Japan) |